Linux Driver Project
CS572, Fall 2010
Remi Auduon
Nathan Collins
Jim Larson
Harry Pan
Andrew Sackville-West

---
Exciting Applications !
Userland
Devices
Kernel
USB
Elegance and Innovation
Handlers
Teensy HW/SW
HW Attached to Teensy
Creative Circuitry
Boring Drivers => Exciting Applications!

---
Access thru Teensy:
Three Color LED
LED Indicators
ADC Devices: Teensy Port F0 thru F5
Motor Controllers: Teensy Timer/Counter in PWM Mode
        Plus Two Port pins to H-bridge
Teensy Hardware

---
Goal: Provide Abstract Interface for device access
Transparent access for modular devices
Single entry point for all uses – teensy_send()
Arbitrary data (within limits) with a simple multiplexing scheme
New modules are sheltered from USB
Request-Response scheme
Requests are tagged and submitted to Teensy
Responses return with the same tag
Requests block pending results from Teensy
Future Work
Error-handling – prevent permanently blocked processes
Teensy driven enumeration of devices
Device-specific mutual exclusion
Driver Core

---
Modular modules
Goal: easy addition of submodules
Ignore usb and core system
ignore other submodules
Solution
Kernel land: standalone driver
HW land: handler
Comm system marshals messages
User Device Driver

---
Example Program: Sensing ambient light level
Example Program: Monitoring system load
fp = fopen("/proc/stat", "r");
fgets(buffer, 255, fp);
sscanf(buffer, "cpu %llu %llu %llu %llu %llu %llu %llu %llu",
        &usertime, &nicetime, &systemtime, &idletime,
        &ioWait, &irq, &softIrq, &steal);
...
double cpu = MIN(100.0, MAX(0.0, ((nicePeriod + userPeriod +
systemAllPeriod) / totalPeriod * 100.0)));
User Applications – Reading the Environment

---
Innovation in Driver Architecture
USB Monitor to User Devices
Access to Hardware thru Teensy
Boring Drivers enable Exciting Applications
Linux Driver Project Summary